WESTERN					    FORMULA ANTI-CLOG® #1

WATER 					          DRIP PAN BIOCIDE

ASSOCIATES

PRODUCT DATA SHEET

DESCRIPTION    	Formula ANTI-CLOG® # 1  is a ready to use packaged biocide specifically developed for industrial drip pan applications including, air conditioning and refrigeration applications, This product is safe to handle and easy to apply.  It has a 3 month activity period per application.

AIR CONDITIONING APPLICATIONS:

ANTI-CLOG® # 1 PLACEMENT:

FT/C: FOR EQUIPMENT UP TO 5 TONS.

AT/C: FOR EQUIPMENT OVER 5 AND UP TO 15 TONS. NOTE: FOR LARGER EQUIPMENT USE MULTIPLE UNITS.

IMPORTANT:
DO NOT USE in Humidifiers, Humidifier Sections In Air Conditioning Systems Or Evaporative Coolers IF Heat Lamps Sit Directly Over Or Near Drain Pan Where The Anti-Clog® #1 Has Been Installed.

REFRIGERATION:

ANTI-CLOG® #1:

AIR CONDITIONING - REFRIGERATION DRAIN PAN MAINTENANCE PRODUCTS

CONTROL:

- SLIME BUILD-UP AND CONSEQUENT DRAIN PAN OVERFLOWS

- THE GROWTH OF HARMFUL BACTERIA INCLUDING THOSE CAUSING LEGIONNAIRE'S DISEASE

- MUSTY ODORS INTRODUCED INTO AIR HANDLING UNITS FROM BACTERIAL SLIME ACCUMULATIONS.

IMPROVED CHEMICAL FORMULATION:

- 40% High efficiency biocide (by weight).

- Laboratory proven 99% kill of Legionnaire's Disease Bacteria (LDB).

- Combats a broad spectrum of harmful bacteria including those causing the common cold and other respiratory ailments.

- pH neutralizers help protect pan against corrosion.

- EPA registered.

- 3 month, 24 hours/day service life in all climates.

- Consistent ppm release per day.

FUNCTIONAL DESIGN

- Sealed, tamper proof housing prevents skin contact with biocide.

- Filter pad meters biocide for consistent chemical release.

- Water saturated filter pad and weight prevent flotation.

- Designed NOT to clog drain hole.

- Can be placed either vertically or horizontally.

- Low profile - fits most cooling equipment.

Place ANTI-CLOG® under cooling coils in middle of pan length. It goes to work immediately upon contact with water!

The Anti-Clog®, is designed and approved only for use in drain pans of Air Conditioning Systems and Refrigeration Systems.

HERE'S WHAT THE CITY OF NEW YORK DEPARTMENT OF HEALTH SAYS ABOUT EPA REGISTERED BIOCIDE FEEDERS:
"Fan-coil units and air handlers should be equipped with an EPA registered biocide feeder or treated with an EPA registered biocide formulated for this purpose. These are designed to inhibit bacterial growth, prevent clogging of the condensate drain system and prevent odors. Such treatment is considered to be consistent with good engineering practices". (From a report issued by Commissioner R. Ferrer, M.D.)

WHY is the Anti-Clog® # 1 needed?

1. CONDENSATION

Cooling equipment produces cold air by passing warm air over cooling coils. This cooling action causes condensate (water droplets) to form and drip off the cooling coils, similar to the droplets formed on the glass of a cool drink on a hot day!

Have you ever seen water dripping out of a window air conditioner? This is a common example of condensation.

2. DRAINAGE



In large commercial cooling equipment, condensate cannot be allowed to drip out onto passersby or other objects. Therefore the condensate must be collected in a drain pan inside the unit. When enough droplets collect, the condensate begins flowing to a drain hole. IT IS HERE IN THE DRAIN PAN THAT POTENTIAL TROUBLE BEGINS!

3. BACTERIA

Bacteria, naturally present in water including condensate, produce "SLIME" as a waste product.

ACCUMULATIONS OF SLIME CAN:

- Block the drain hole, causing the drain pan to overflow, resulting in costly flood damage.

- Provide an ideal breeding ground for harmful bacteria including those causing the common cold, asthma, fatigue, headaches, flu, allergies and the deadly Legionnaire's Disease.

The Anti-Clog® # 1 Kills Slime and Disease-Producing Bacteria!

WHERE is the Anti-Clog® # 1 needed?

- SCHOOLS/UNIVERSITIES

- HOTELS/MOTELS

- HEALTH CLUBS

- HOSPITALS

- APARTMENT BUILDINGS

- OFFICE BUILDINGS

- NURSING HOMES

- SUPERMARKETS

WHEREVER AIR CONDITIONING/REFRIGERATION IS USED!!!

WHEN is the best time to install the Anti-Clog® # 1 ?

FOR OPTIMAL PERFORMANCE:

Initial placement:
     Install the ANTI-CLOG® #1 during preseason maintenance programs prior to system start-up.

Follow-up maintenance:
     Replace the ANTI-CLOG® #1 every 3 months for the duration of the cooling season.

Following this recommended usage program will protect buildings from:

- Drain pan overflow resulting in costly flood damage.

- The spread of harmful bacteria bred in drain pans.

HOW does the Anti-Clog® # 1 work?

The ANTI-CLOG® #1 is a biocide (quaternary ammonium) tablet enclosed in a plastic housing. Ultrasonically sealed to the housing is a white filter pad. Water is absorbed by the filter pad and "wicked" to the tablet.

The release of powerful biocide is initiated as the water begins dissolving the tablet. The filter pad controls the release of biocide resulting in a 3 month service life in even the hottest and most humid climates!

The ANTI-CLOG® #1 works either horizontally or vertically at angles up to 60°, without compromising performance.

WHY is the Anti-Clog® # 1 a superior product?

- It contains the highest amount of active biocide of ANY product on the market!

- It is the ONLY product on the market permitted by the EPA to make a Legionnaire's Disease Bacteria (LDB) kill claim!

- The filter pad meters a consistent biocide release for a 3 month service life!

- Its safe to use, sealed, tamper-proof housing prevents contact with biocide!

- It is EPA registered!

ANTI-CLOG® #1: INEXPENSIVE HEALTH PROTECTION AND PREVENTATIVE MAINTENANCE!

In laboratory tests the Anti-Clog® formulation has been shown to inactivate pure cultures of Legionnaire's Disease Bacteria (LDB). The ability of this formulation to control the growth of or inactivate LDB in air conditioning condensate drain pans exposed to organic material and other microbial contamination has not been documented.

A direct relationship between the presence of this bacteria and the potential for human disease has not yet been proven.

SPECIFICATIONS:

CHEMICAL SPECIFICATIONS:
Active ingredients:
Alkyl (60% C14, 30% C16, 5% C12, 5% C18) Dimethyl Benzyl Ammonium Chloride - 20%
Alkyl (68% C12, 32% C14) Dimethyl Ethylbenzy] Ammonium Chloride - 20%
Inert Ingredients: 60%

MECHANICAL SPECIFICATIONS:
FT/C - 2 3/4" long x 2 1/4" wide x 1/2" high, contents 3/4 oz.
AT/C - 3 5/8" long x 2 3/4" wide x 7/8" high, contents 2 1/8 oz.

NOTE: Not for use in applications exceeding 150°F. ____________________________________________________________

©2004 Western Water Associates, Inc.  All rights reserved.  For more information call (831) 607-9770	 PDSAntilog(2/12)